## Slide 1
Peter Le
Email: peter.le@visionaustralia.org
Round Table 2021
Information Access – Innovation and Collaboration
UV Printing: the future of Tactile graphics

## Slide 2: Who am I?
Team Leader of Transcriptions at Vision Australia
Over 22 years working with print accessibility
Background in Biology and Organic Chemistry
Experienced in programming, graphic design and adaptive technology
Fluent in using and producing Braille, can read by touch and by sight
Has been apart of many RoundTable production workgroups
Plays the Panflute and Harp

## Slide 3: Overview
What is UV Printing?
How It Works
The Electromagnetic Spectrum
What Can a UV Printer Print On?
The Benefits of a UV LED Printing Machine
Pros and Cons
Layering of images
Types of UV printers
VA Transcription testing and progress

## Slide 4: What is UV Printing?
UV printing is a form of digital printing that uses ultra-violet lights to dry or cure ink as it is printed. As the printer distributes ink on the surface of a material (called a "substrate"), specially designed UV lights follow close behind, curing - or drying - the ink instantly. Originally developed for quickly drying gel nail polishes during manicures, ultraviolet light applications quickly expanded into industrial and commercial markets. Because the UV lights cure any printed ink immediately, the dots of wet ink do not get a chance to spread out once printed, resulting in much finer detail. In addition, UV cured inks are weather-resistant and offer increased resistance to fading. This curing process is more environmentally friendly as it produces few VOC’s, odor, and heat.
https://www.displays2go.com/Article/UV-Flatbed-Printing-53

## Slide 5: How It Works
UV curing involves a photo-chemical reaction which converts a liquid or semi-liquid organic compound to a hard plastic-like polymer. The heart of this reaction is a special compound, known as a "photoinitiator", which absorbs light and then uses the absorbed light energy to initiate and propagate the curing reaction.
Other printing processes requires heat to vaporise water or solvents. UV curing involves a total conversion of liquid material to a solid state.
The UV curing process is very fast, usually completed in fractions of a second. This means reduced space requirements. Racking or secondary drying operations are eliminated with UV curing.
Any UV curing process requires a UV light source and a specially design formulation for the UV curing process. Both the light source and the UV curable material are normally designed for each specific application.

## Slide 6: UV ink curing
http://www.bul.com.hk/bul/en/technologies/uv_curing

## Slide 7: Another image of UV Curing
http://www.brancher.com/-Sechage,41-.html?lang=en

## Slide 8: The Electromagnetic Spectrum
UV lamps emit in different UV ranges in order to have maximum drying efficiency.
UV-C (200-280 nm) activate the photoinitiators and assure surface drying.
UV-B (280-315 nm) maintain the polymerisation reaction.
UV-A (315-380 nm) assure in-depth drying.
http://www.brancher.com/-Sechage,41-.html?lang=en

## Slide 9: What Can a UV Printer Print On?
Any non absorbent surface.
Plastics, glass, metal, wood, fabric, paper … the list is endless
The main issue is how long will it adhere to the material?
Primers can be used to improve how well the UV print can adhere to material
Gloss ink adheres best as the UV light can penetrate further into the ink

## Slide 10: The Benefits of a UV LED Printing Machine
UV printing offers a new way of tactile production
Faster than 3D printing
Roland UV printer has flexible ink
It’s a clean and precise finish
Long lasting and durable
Full colour print
Can be printed on most objects and materials
Quality printing
UV printing is considered a green technology, safe for the environment and leaving an almost zero carbon footprint.
UV inks dry on contact, they never smudge.

## Slide 11: Pros and Cons
Pro
Can print on most surfaces
Great for fabricating already made items
Mass production of small units
Can print white or over print mistakes
No guess work, will always print the same quality
Photo quality colour printing
Cons
    Slower than swell paper
    Not a standard office product
    Niche area – specific support
    Cost of Machine

## Slide 12: Types of UV printers
Large Format UV Printers
Flat Bed UV Printer
UV 3D printer
UV Resin 3D printer
UV Printer Cutters

## Slide 13: Layering of images
To make UV printing effecting, we use it like a 3D.
By printing multiple levels.
Gloss works best for building layers
All colours work, at varying heights.
Using multiple print heads
Print order matters

## Slide 14: Layering of images – example
Source https://gjs.co/courses/e30/understanding-uv-printing

## Slide 15: VA Transcription testing and progress
Where to start?
What materials to try first?
Colour test
Gloss test
Layered test
Lines and textures
Layering of images
Transparency

## Slide 16: Lines, how do they work
Line thickness: Solid lines and line patterns

## Slide 17: Finger prints – line quality

## Slide 18: Swell paper cross over

## Slide 19: Tactile colouring pictures

## Slide 20: Braille Music – using different line thickness to build layers

## Slide 21: Floor plan section – using 3 layers to create a multilevel map

## Slide 22: Floor Plan – final print

## Slide 23: Europe typographical map – 7 layers

## Slide 24: Australia – 3 level map

## Slide 25: Australia printed map

## Slide 26: Bat skeleton – white gloss print

## Slide 27: Stegosaurus

## Slide 28: Spider – using transparency
How to have one print and still create a layered image

## Slide 29: Ember – 4 layers

## Slide 30: Vadrik and Rob – work of art

## Slide 31: Dreams
Chinese Factory of UV printers

## Slide 32
Any questions?
Thank you
Peter Le Email: peter.le@visionaustralia.org
We offer free transcription to Clients of Vision Australia under our Personal Support service which is a free service that is funded by the Federal Government's Print Disability Grant. This service is for personal use.
For more information on accessible format conversions, email: printaccess@visionaustralia.org or call 1300 84 74 66
Notes: Does anyone have any questions?